## Slide 1: Island City On a Wedge
Paper Discussion James Doss-Gollin

## Slide 2: Galveston, 1900
Notes: Target: 1:00. Open with the deadliest natural disaster in US history. Don’t linger—move to the problem they faced.

## Slide 3
Source: Galveston Historical Foundation
September 8, 1900: Category 4 hurricane, 8,000+ deaths
The response:
17-foot seawall (still standing)
Raised the entire city by up to 17 feet
Moved thousands of buildings
The question: Build a wall? Raise the land? Retreat? All three?

## Slide 4: ICOW: The Middle Path
ICOW = Island City On a Wedge (Ceres et al. 2019)
Fast: evaluate millions of strategy combinations
Rich: graduated damage (not binary)
Flexible: portfolios of defenses (wall + retreat + elevate)
Key insight: You don’t need every street corner—just the right abstraction.
Notes: Target: 1:03. Introduce ICOW as the solution.

## Slide 5: How ICOW Works
ICOW takes city geometry + defense choices → computes expected damages. Source: Ceres et al. (2019)
Notes: Target: 1:07. High-level overview of inputs and outputs. We’ll unpack each piece over the next slides.

## Slide 6: The Wedge Geometry

## Slide 7: Picture a Coastal City
Notes: Target: 1:08. Build intuition for why the wedge is a good abstraction. The ICOW paper uses Lower Manhattan as its case study.

## Slide 8
The ICOW paper was modeled after Lower Manhattan. Source: Ceres et al. (2019)
What do coastal cities share?
Waterfront at low elevation
Terrain rises inland
Density highest near water

## Slide 9: The Wedge Abstraction
The wedge geometry captures essential features. Source: Ceres et al. (2019)
Notes: Target: 1:10. Explain the geometry. These are the parameters students will estimate in the activity.

## Slide 10: What Gets Flooded?
Notes: Target: 1:12. Use the wedge figure to build intuition about zone-based damage. Pause after each question to let students think before revealing answer.

## Slide 11
Source: Ceres et al. (2019)
If water reaches Zone 4—what’s the damage?
→ Three zones underwater (large fraction of city value)
If water reaches Zone 3?
→ Zero… unless the dike fails
What happens when dikes fail?

## Slide 12: Key Parameters
Parameter | Symbol | Meaning
Maximum elevation |  | How high does the city rise?
City depth |  | How far inland does the city extend?
Coastline length |  | How long is the waterfront?
Seawall height |  | Existing protection height
Notes: Target: 1:14. These are the parameters you’ll estimate in the activity. Values are from the ICOW paper—ask students if they seem reasonable.

## Slide 13
From the paper (Manhattan): m, km, km
Do these seem reasonable? (We’ll check in the activity.)

## Slide 14: The Five Defense Levers
Lever | What it does | Real-world example
Withdrawal () | Vacate low-lying land | Managed retreat, buyouts
Dike Base () | Where the wall starts | Seawall location
Dike Height () | How tall the wall is | Seawall height
Resistance Height () | Flood-proof buildings | Elevating structures
Resistance Fraction () | What % of buildings | Retrofit programs
Notes: Target: 1:15. Key vocabulary. Students don’t need to memorize—just recognize.

## Slide 15
The key constraint:
You can’t withdraw past the city limits, and you can’t build a dike taller than the land behind it.

## Slide 16: The Economics

## Slide 17: Damage Isn’t Binary
Simple models say: flood = total loss, no flood = zero.
Reality: A 1-foot flood ruins your carpet. A 10-foot flood destroys the structure.
ICOW computes damage based on volume flooded:
The 0.39 is an empirically-derived depth-damage parameter: the fraction of zone value destroyed at full inundation (from flood damage curves).
This connects to Monday’s EAD formula (Week 4 lecture)—but now we can compute damage for any surge height.
Notes: Target: 1:17. Contrast with simple models. Key insight: damage depends on what’s underwater and how deep.

## Slide 18: Dikes Aren’t Perfect
A dike doesn’t magically hold until overtopped, then fail.
Fragility curve: Failure probability ramps up as water approaches the crest
Water below 95% of crest: very low failure probability
Water at 95%+: failure probability ramps linearly
At 100%: certain overtopping
The levee effect: People behind dikes often don’t evacuate. If the dike fails, they’re caught off guard. ICOW models this: damage behind a failed dike is 1.3× worse than open flooding.
Notes: Target: 1:19. The fragility curve is intuitive. This creates interesting risk trade-offs.

## Slide 19: Activity: Map Your City

## Slide 20: The Task
Work in pairs. Use Google Maps to estimate ICOW geometry parameters for a real coastal city.
You’ll need:
Google Maps with terrain view
ICOW.jl documentation: https://dossgollin-lab.github.io/ICOW.jl/equations.html#parameters
Notes: Target: 1:21. Clear instructions. Make sure everyone has Google Maps open.

## Slide 21: Make a Prediction
Before we look anything up—take 30 seconds:
Which city do you think has the steepest geometry? (highest ratio)
Notes: Target: 1:23. Quick prediction to create cognitive investment before the activity. Have students write down a guess before seeing any data.

## Slide 22
Miami Beach
Galveston
New Orleans
Rotterdam
Mumbai
Venice

## Slide 23
Write down your guess. We’ll check later.

## Slide 24: Pick a City
Notes: Target: 1:25. Assign cities if students hesitate: “Table 1 takes Miami, Table 2 takes Rotterdam…”

## Slide 25
Galveston, TX
Miami Beach, FL
New Orleans, LA
Boston, MA
Mumbai, India
Jakarta, Indonesia
Lagos, Nigeria
Shanghai, China

## Slide 26: Estimate These Parameters
Parameter | How to Estimate
 | Elevation change: waterfront → highest urban point
 | Horizontal distance: waterfront → highest point
 | Length of exposed coastline
 | Existing protection height (search online)
Notes: Target: 1:27. Give 6 minutes for estimation. Students need ALL four parameters for Friday’s lab.
Circulate and address common issues: - “Where does the city end?” → Focus on the flood-prone coastal zone, not the whole metro area - “I can’t find elevation” → Try Google Earth, or search “[city] topography” - “What’s a seawall?” → Any hard barrier at the water’s edge - “My city has no seawall” → Use 0m. The model handles this—it just means no existing protection. - “The terrain isn’t really a wedge” → Focus on the flood-prone coastal zone, not the whole metropolitan area. Most waterfronts approximate a wedge locally.

## Slide 27
Tools: Google Maps terrain view, Google Earth elevation, Wikipedia
You’ll need all four parameters for Friday’s lab!

## Slide 28: Share Out
Pair up with a table that studied a different city:
Compare your ratios
Which city is steeper? Which is flatter?
What does that imply for dike strategy?
Class discussion: A steep city vs. a flat city—who benefits more from a 3m dike?
Notes: Target: 1:33. Call time. Facilitate cross-table comparisons. Look for interesting contrasts (e.g., Miami vs. Rotterdam, steep vs. flat cities).

## Slide 29: Key Takeaways
ICOW abstracts complex cities into a few key parameters
The wedge geometry captures essential physics: higher surges flood more area
Different cities → different optimal strategies
Friday’s lab: You’ll use ICOW.jl to compute EAD for a single year
Notes: Target: 1:41. Debrief: “Notice how different geometries suggest different strategies.”

## Slide 30: Preview: Friday’s Lab
Friday we’ll implement single-year EAD analysis:
Use the same parameters you estimated today
Add a storm surge distribution
Compute expected annual damage
Explore how the five levers change EAD
Notes: Target: 1:44. Brief preview.

## Slide 31: One More Thing…
Rotterdam is 6 meters below sea level.
How does ICOW even work there?
(We’ll find out Friday.)
Notes: Target: 1:47. Hook for Friday—leave them thinking.

## Slide 32: References
Ceres, Robert L., Chris E. Forest, and Klaus Keller. 2019. “Optimization of Multiple Storm Surge Risk Mitigation Strategies for an Island City On a Wedge.” Environmental Modelling & Software 119 (September): 341–53. https://doi.org/10.1016/j.envsoft.2019.06.011.