## Slide 1: Global Sensitivity Analysis
Lecture Dr. James Doss-Gollin

## Slide 2: Reading
Sensitivity Analysis: The Basics from Reed et al. (2022)
Pianosi et al. (2016)
Saltelli et al. (2008)

## Slide 3: Two Questions About Uncertainty
VOI: Which uncertainty, if resolved, would most change my decision?
GSA: Which uncertainty contributes most to the variability in my output?
These are not the same question, and the answers can disagree.
Notes: “We just covered VOI. Now I want to introduce a complementary tool.” Write both questions in different colors. “A parameter can dominate the output variance but have zero EVPI — if it doesn’t change which action is best.”

## Slide 4: What Is Sensitivity Analysis?
SA investigates how variation in a model’s output is attributed to variation in its inputs (Pianosi et al. 2016).
Which inputs cause the largest variation in ?
Are there inputs whose variability has negligible effect?
Are there interactions between inputs?
Notes: “We have a model — could be your dike model, a climate model, an economic model. It takes uncertain inputs and produces an output. SA asks: which inputs matter?”

## Slide 5: Three Purposes of SA
Screening (factor fixing): which inputs can I safely ignore?
Ranking (factor prioritization): which input matters most?
Mapping: what input combinations produce extreme outputs?
Typical workflow: screen → rank → map.
Notes: “Start cheap — screening tells you which inputs to throw out. Then rank the rest. Mapping is the most expensive but most useful for decision-making.” “For your final project, you’ll want to do at least ranking.”

## Slide 6: Local Sensitivity: One-at-a-Time
Vary one input at a baseline , hold all others fixed:
Approximate with a finite difference ( evaluations):
Notes: “You’ve already done this — in Lab 5 you ran RCP 8.5, then RCP 2.6. That’s OAT.” “It’s cheap and gives you a quick first look. But it has problems.”

## Slide 7: OAT Limitations
Measures sensitivity at one point — may differ elsewhere
Misses interactions between parameters
Baseline choice is arbitrary
Does not explore the full input range
Notes: Ask: “What’s the problem with changing one thing at a time?” Sketch 2D input space: SLR on one axis, discount rate on the other. OAT only explores the cross through the center. Global SA fills the whole square.

## Slide 8: Going Global
Global SA varies all inputs simultaneously across their full ranges.
Captures the full range of each input
Detects nonlinear effects
Captures interactions between inputs
Two representative methods: Morris (OAT from many starting points) and Sobol indices (variance decomposition).
Notes: “Global doesn’t mean you can’t do OAT. Morris does OAT from many random starting points. The key is covering the full input space, not just one baseline.”

## Slide 9: The Morris Method (Elementary Effects)
Repeat the local finite difference from random starting points. For each input and trajectory :
Summarize across trajectories:
Mean of : overall influence (ranking)
Std. dev. of : interactions or nonlinearity
Cost: evaluations (e.g., for ).
Notes: “Morris is just the local calculation repeated from many different starting points. Then you look at how the sensitivity changes across the input space.”

## Slide 10: Reading a Morris Plot
Figure 1: Source: Pianosi et al. (2016), Appendix A.

## Slide 11
Near origin: unimportant — screen out
Far right, low SD: strong main effect
Far right, high SD: important and interactive
Notes: “This one plot tells you everything. Near the origin — doesn’t matter, throw it out. Far right — it matters. If the SD is also high, it’s interacting with other inputs.”

## Slide 12: Variance Decomposition
For independent inputs, the total variance decomposes:
: main effect of
: interaction between and
Higher-order terms exist but are rarely important in practice
Notes: “The total variance of the output splits into pieces: how much comes from each input alone, how much from pairs interacting, and so on. In practice, first-order and second-order terms capture nearly everything. You’ll rarely see higher-order interactions reported in the literature.”

## Slide 13: Sobol Indices
First-order — if you knew , what fraction of the variance in would go away?
Total-order — if you knew everything except , what fraction of the variance would remain?
where denotes all inputs except .
Notes: “S_i: if you could pin down this one input, how much would your uncertainty in the output shrink? That’s the main effect. S_{T_i}: if you pinned down everything else, how much uncertainty would be left? That captures the input’s main effect plus all its interactions. If S_i \approx S_{T_i} for every input, the model is approximately additive — no interactions.” Go slowly — this is the most notation-heavy part.

## Slide 14: Interpreting Sobol Indices
Pattern | Interpretation
large, | Strong main effect, few interactions
small, large | Matters mainly through interactions
small, small | Doesn’t matter much
 | Model is mostly additive

## Slide 15
Screening rule: is necessary and sufficient for unimportance (Pianosi et al. 2016).
Notes: “This table is your cheat sheet for reading Sobol indices.” Walk through each row with a concrete example from the dike problem.

## Slide 16: Reading a Sensitivity Analysis
Three questions to always ask:
What inputs were varied? Different scope → different results
What distributions were assumed? Change the distribution, change the indices
Are the results converged? Finite samples give estimates, not exact values
Notes: “If someone hands you a sensitivity analysis — or you’re doing one yourself — this is your checklist.”

## Slide 17: The Distribution Assumption
Every GSA calculation requires a probability distribution .
gives different Sobol indices than .
“The definition of the input variability space is one of the most delicate steps in the application of GSA.” — Pianosi et al. (2016)
Notes: “This is the punchline, and it connects back to VOI. Both VOI and GSA require probability distributions over the inputs. When you can’t specify those distributions confidently — that’s deep uncertainty. That’s Week 8.”

## Slide 18: Summary
VOI: which uncertainty affects the decision?
GSA: which uncertainty affects the output?
These are not the same — answers can disagree
Both require probability distributions over inputs
When you can’t specify distributions → deep uncertainty (Week 8)
Notes: “Two complementary tools, same requirement. Next week we break that requirement.” “Friday’s lab puts VOI to work on a house elevation problem under sea-level rise uncertainty.”

## Slide 19: References
Pianosi, Francesca, Keith Beven, Jim Freer, Jim W. Hall, Jonathan Rougier, David B. Stephenson, and Thorsten Wagener. 2016. “Sensitivity Analysis of Environmental Models: A Systematic Review with Practical Workflow.” Environmental Modelling & Software 79 (May): 214–32. https://doi.org/10/f8n6zw.
Reed, Patrick M., Antonia Hadjimichael, Keyvan Malek, Tina Karimi, Chris R. Vernon, Vivek Srikrishnan, Rohini S. Gupta, et al. 2022. Addressing Uncertainty in Multisector Dynamics Research. Zenodo. https://doi.org/10.5281/zenodo.6110623.
Saltelli, Andrea, Marco Ratto, Terry Andres, Francesca Campolongo, Jessica Cariboni, Debora Gatelli, Michaela Saisana, and Stefano Tarantola. 2008. Global Sensitivity Analysis: The Primer. John Wiley & Sons, Ltd. http://onlinelibrary.wiley.com/doi/abs/10.1002/9780470725184.ch1.